22.12.2021

NABÍDKA – A20-LEV-NSF0323 VŘ

| Nabídka pro: | Nabídka od: |
| --- | --- |
| Vysoká škola chemicko-technologická v Praze Veřejná vysoká škola Praha 6, Dejvice, Technická 1905/5, PSČ 166 28 Nabídka do výběrového řízení: Mikroskop atomárních sil (AFM) | ANAMET s.r.o. xxxxxxxx Kováků 26 150 00 Praha 5 Tel.: xxxxxxxxxx xxxxxxxxxxx |

| Item No. | Article |
| --- | --- |
| BT05886 | NaioAFM All-in-One AFM for Nanoeducation and Small Samples • Integrated controller, XY-table, airflow shielding, and vibration isolation • High resolution top view camera and side view sample observation built in • Feature-complete: All standard operating modes available • Simple cantilever exchange: no laser or detector adjustment required • No system setup needed: just plug into your PC and start the software • User-friendly software wizards quickly prepare measurement parameters sample size: max. 12x12mm, 3.5mm height XY positioning range: 12mm travel in X and Y automatic approach: 4mm linear motor, continuous or step-by-step approach top view camera: 2 mm × 1.5 mm FOV, 2 μm optical resolution, 5.0 MPixel color CMOS, 4× digital zoom, in-axis LED illumination Scan range XYZ: 70 µm x 70 µm x 14 µm Z Drive resolution: 0.2 nm XY Drive resolution: 1.0 nm Z noise level: typ. 0.4 nm (RMS, static mode in air) Z noise level: 0.3 nm (RMS, dynamic mode in air) Imaging modes: Static Force Advanced Imaging modes: Dynamic Force, Phase Contrast, MFM, EFM (requires Naio Dynamic Modes Option) Spreading Resistance, Force Modulation (requires Naio Advanced Modes Option) Spectroscopy modes: Force–Distance, Tip Voltage–Deflection Advanced spectroscopy modes: Amplitude–Distance (requires Naio Dynamic Modes Option), Current–Voltage (requires Naio Advanced Modes Option) Stop by end value, Fwd & Bwd pause (requires Naio Spectroscopy and calibration Option) Lithography modes: Static Force, Oxidation Advanced lithography modes: Dynamic Force (requires Naio Dynamic Modes Option), Draw and load CAD vector graphics, Bitmap images (requires Naio Advanced Modes Option) Contents: - NaioAFM - Control Software - Operating Instructions Manual - Tool set - Instrument case - Power supply - Power cable - USB Cable |
| BT05881 | NaioAFM Dynamic Modes Option This NaioAFM Option provides the following additional features: - Additional Imaging modes: Dynamic Force, Phase Contrast, MFM, EFM - Additional spectroscopy modes: Amplitude–Distance - Additional lithography modes: Dynamic Force Contents: - Document with license key |
| BT06396 | Naio Advanced Modes Option - Advanced imaging modes (NaioAFM only): Spreading Resistance (including current voltage-spectroscopy), Force Modulation - Advanced lithography modes: Draw and load CAD vector graphics, Bitmap images - Remote control/add-ons: Windows scripting interface: compatible with LabView, C#, Visual Basic, MatLab, and other software... Contents: - Document with license key |
| BT06397 | Naio Spectroscopy and Calibration Option - Advanced spectroscopy modes: Stop by end value, Fwd & Bwd pause - Cantilever calibration by Sader method and frequency sweep (NaioAFM only) Contents: - Document with license key |
| BT05171 | Isostage Adapter for NaioAFM/STM The adapter are used to mount the NaioAFM or NaioSTM on top of the Nanosurf Isostage vibration isolation platform. No screws has to be fixed and mounting/unmounting can be done with ease. Contents: - Set of 4 adapters |
| BT06371 | Isostage 300L Active vibration isolation table Max. load: 2-12 kg Dimensions: 300 x 300 x 80 mm Frequency range active: 1 - 200 Hz Isolation power: min. 23 dB (93.0%) at 5 Hz, 40 dB (99.0%) above 15 Hz SpikeGuard for detection of out of range disturbances and correction thereof Contents: Isostage 300L damping table Isostage controller connection cable to AFM controller power cable tools and screws |
| tr | Zahraniční dopravné, celní polatky |
|  | Cena v Kč celkem s dodáním na paritě DDP bez DPH: | 1 107 962,00 |
|  | DPH 21%: | 232 672,02 |
|  | Cena celkem s dodáním na paritě DDP včetně DPH: | 1 340 634,02 |

#### OBCHODNÍ PODMÍNKY

Obchodní podmínky jsou v souladu se zadávací dokumentací a nabídka je platná po celou dobu zadávacího řízení.