TECHNICAL RIDER - MOONDANCE ORCHESTRA 2023

PROFESSIONAL P.A. System : 1 person /min 10 W

FRONT OF HOUSE

PA SYSTEM:

NEXO, L-ACOUSTIC, d&b, MAYER SOUND

NO ACCEPT: home made system, JBL –VRX, JRX, PRX, STX, EON… dB technology, AC Akustika !!!!!!

CONSOLE: 32 INPUT digital professional console pref. YAMAHA CL-QL-PM 3/5/7

CONTROL:	Intercom stage-FOH + talkback

------------------------------------------------------------------------------

MONITORS

CONSOLE:     32 INPUT analog or digital professional console

DYNAMICS:   4x channels compressor

FX:		        1x reverb/hall

WAYS:	        the mixer needs min. 11 Aux sends (11x separate ways) 		        13x floor monitors

EQ:		         9x 31 band EQ

WEDGES:       13x professional cabinets -pref. Nexo 45n12, NexoPS 10,15, L-Ac. 115FM/Hi Q, etc...

(4x solo voc, 1x drums, 1x perc, 1x bass+gtr, 1x keys 1, 1x keys 2, 4x brass) + 2x mono InEar mon. (vlastní-own)

------------------------------------------------------------------------------

Prosím o pečlivé prostudování !  No accepted  znamená : NEBUDE AKCEPTOVÁNO,  děkujeme předem!!!

Moondance Orchestra vystupuje vždy s vlastním FOH zvukařem.

Profesionální monitorový zvukař a podiový technik je z dodavatelské RENTAL společnosti.

Mixážní pult musí být umístěn v sále, nikdy na balkóně, pod balkónem, v lóži atp.

V případě nejasností nebo konzultací mě prosím kontaktujte.For question call, or write